## Slide 1: Triggered Guitar Effects Platform
Ralph Carlo Quinto (CE), Bryan Guner (EE), Haley Scott (EE)
Advisor: Dr. Ambrose Adegbege

## Slide 2: Overview
Problem Identification
Project Goals
Project Status
Pure Data
Video Demonstration
Digital Effects
Dynamic Time Warping
Project Management
Summary

## Slide 3: Problem Identification
Guitar effect pedals physically restrain the guitar player
Effect pedals require presence of mind on the part of the performer
Analog and digital effects pedals are costly
Notes: Explain in detail how electric guitar works
-Mention Effects pedals require presence of mind on the part of the performer to trigger them at the correct time, and to adjust the settings between songs or even between sections of songs
-Explain that these constraints limit the performer’s mobility and stage presence and split their focus away from playing their instrument
-Explain that digital effect software is a more cost effective option

## Slide 4: Project Goals
Develop a software platform to analyze a time sequence of notes and trigger guitar effects as instructed
Consistently tolerate error in performance and recognize trigger points
Mitigate the latency between a detected match and the triggering event
Process sequences up to 10 note onsets per second

## Slide 5: Team Breakdown
Bryan Guner | Team Lead - Develop a protocol for digital signal processing of the guitar signal in order to create a time-sequential record of the frequency content of the guitar signal and a comparison between pre recorded songs and live performances.
Ralph Quinto | Software Engineer - Research for possible programming platforms. Responsible for reading electric guitar signals, creating the signal analysis patches in pure data, and triggering digital guitar effects.
Haley Scott | Architectural Manager - Responsible for ensuring successful integration of project components, researching system methods, designing digital effects, Project and Organizational Management

## Slide 6: Project Status
Purchased components
Created simplified guitar effect trigger patch
Generated digital guitar effects
Began the implementation phase of Dynamic Time Warping

## Slide 7: Background (Pure Data)
Visual programming language (LabView)
  Objects are linked together to model the flow of control and audio
  Designed for creating interactive computer music and multimedia works.
    Generate Waveforms
    Perform Signal Analysis
Modular code base
  Externals could be generated using C, C++, Python, Java, and many more
Open source project listed under a modified BSD License
  all distributed copies of the source code must contain the BSD license

## Slide 8: Project Specs (PD & Physical Components)
Pure Data Specs
  Sampling rate of 44,100 Hz
  Block size of 1024
Electric Guitar: Ibanez RG5EX1
  Bridge Pickup: Infinity 4
    Magnet: Ceramic
    DC Resistance: 15.6 KΩ
  Gauges: .009/.011/.016/.024/.032/.042

## Slide 9: Current PD Implementation

## Slide 10: Block Diagram of Simplified PD Patch

## Slide 11: Video Demonstration

## Slide 12: Issues With Approach
Sensitive to performance speed and articulation
Similar songs may trigger an effect configured for a specific song
Minor inconsistencies in count accuracy
Geared towards handling 1 note at a time

## Slide 13: Delay Effect
Creates the sound of a repeating, decaying echo
Delwrite block allocates memory for a delay line
Delread block reads the signal from a delay line

## Slide 14: Fuzz Effect
Creates the sound of a distorted, heavier guitar
Clip block restricts a signal to lie between two limits

## Slide 15: Reverb Effect
Creates the sound of a performance in a concert hall
Mirrors a large number of reflections to build up and then decay
Notes: freeze function allows you to grab any section of your active reverb tail in real time and add continuous sustain

## Slide 16: Dynamic Time Warping
Algorithm for the measurement of similarity between two temporal sequences
Calculates an optimal match in the form of a distance that is the sum of localized cost functions

## Slide 17: DTW Path
The process can be thought of conceptually as arranging the two sequences on the sides of a grid
Each cell within the grid will be filled in with a distance measure comparing the corresponding elements of the two sequences

## Slide 18: DTW Path

## Slide 19: How DTW Works
To find the best path through the grid, we search for a path that minimizes the total distance between them
Without optimizations, all possible paths through the grid are calculated and a minimum is selected

## Slide 20: Why DTW?
DTW is relatively insensitive to time-scale contraction or dilation in either the database or query signals
A slightly erroneous performance will register a match as long as the section is the closest match to the database sequence relative to what’s been processed so far
The algorithm is commonplace in most speech dictation software and has a wide scope of applications such as gesture recognition

## Slide 21: DTW Data Mining
Find subsequence within a larger database sequence that minimizes DTW-distance to a query sequence over all possible subsequences of the database
Penalizes matches near the beginning or end of the database sequence
Assigns the min DTW-distance that is possible between the query and the subsequence of the database to the ending index of subsequence

## Slide 22: Data Mining Continued
Each subsequence that produces a match will contain a start and end index
Removes all the indices within the nearest local maximums of the subsequences start and end indexes from consideration
Ignores subsequences that are only a slight shift of indices from the best match located nearby
Computational complexity is O(NM)

## Slide 23: Basic Dynamic Time Warping

## Slide 24: Java Implementation

## Slide 25: Block Diagram with DTW

## Slide 26: Project Schedule

## Slide 27: Time Budget

## Slide 28: Spending Budget

## Slide 29: Open Action Items
Create a Dynamic Time Warping Pure Data Object
Design a GUI
Implement ability to apply concurrent effects
Reduce counting inconsistencies

## Slide 30: Summary
Created a simplified automatic guitar effects trigger system
  Capable of triggering Delay Effect
Plan on implementing Dynamic Time Warping Patch
Meeting Design Criteria
  Trigger Latency of <= 1 second
  Minimum Note Onset separation of 10 notes per second
  Concurrent/Multiple Effects Triggering Events

## Slide 31: Questions?